## Slide 1: Bella magspec analysis program
2013/3/19
Kei

## Slide 2: bellaMagspecV01, inheriting from trexSpcMvieV32.
Key concept:
Separate post processing and analysis

## Slide 3: Before scan loop, get global calibrations
For each camera,
Counts -> charge (for 1 GeV, except momentum dependence)
Axis information (except momentum)
Vignette compensation matrix.
Angle uniform axis info.
dP uniform axis info.
Since momentum is proportional to B, all calculation prep for momentum can be done before loop, apply B for each shot inside the shot loop.

## Slide 4: Prepare calibrations in text files.
  Trajectory calibration (4 kinds depending on current)
  Camera calibration (containing all 12 camera information)
  Lanex calibration (to get counts->charge calibration)

## Slide 5: fLanexClb, general function to get Lanex calibratoin
Inputs
  Camera info: FOV, ROI information
  Lanex calibration data
  Screen kind
Outputs
  Count to charge [fC] factor.
  Vignette compensation matrix

## Slide 6: X Axis info
Axis info (non-momentum, out-loop)
Pixel number
Z or x [mm]
Dz or dx [mm]
Electron incident angle on screen [deg]
Path length [m]
Focusing factor x
Focusing factor y
Acceptance low side
Acceptance high side
Momentum [GeV/c] (normalized by B)
Dp/pixel [GeV/c]
After
Charge [fC]
Energy [mJ?]
Noise [fC]
fBellaXAxisAllV01
Calling
fBellaXAxisV01 for axis information.
Input: camera calibration, trajectory calibration

## Slide 7: Clearance
Chamber clearance is 33 mm (+/- 16.5 mm)
Acceptance = clearance / (path x divFY)

## Slide 8: How to solve momentum > inf.?
Neglect for now, 1d interp does now extrapolation.

## Slide 9: Y Axis info
Axis info (non-momentum, out-loop)
Pixel number
y [mm]
Dy [mm]
Axis info (momentum, in loop)
Convert image to angle uniform?

## Slide 10: 2D Axis info
Axis info (non-momentum, out-loop)
Angle [mrad] (x and y dependent)
dAngle [mrad/pixel]

## Slide 11: In scan loop, before image loop
Read log
Make dirs
Allocations
For missed image, fill with 0 image.
Read background, evaluation.

## Slide 12: 3/25, process 3/11 scan11, 4 second/shot

## Slide 14: View and analysis program
Read images (one or three), show it.

## Slide 15: 4/22 summary
Post processing: bellaMagspecV04 is working.
  fBellaImgV01 and fBellaUamCmbV02 might be improved for memory to speed up
Analysis: bellaMagspecViewV02 and bellaMagspecSingleView are working.
Program to analyze average properties to be developed.